## Slide 1: Lab 1: NES Controller

## Slide 2: Types of video game systems
Video game systems can be very complex and use a large number of different processors
Modern video game systems
  Have multi-core CPU
  Have dedicated 3d graphic processor
  Network connectivity, Wired and Wireless
  Optical Drive
  Hard disk

## Slide 3: Our Video Game System
We will focus on something more simple
Look at the technology available in the 1980s
Our system will have limits
  Games will have be small in scope
  2d graphics
  Only have 16 colors (limit of FPGA board)

## Slide 4: Block Diagram – NES System

## Slide 5: Block Diagram – NES system
CPU
8-bit microcontroller
1.79 MHz
Game cartridge
Copy protection
Graphic CPU
PPU 5.37MHz
256x240
Sound Processor
Controllers

## Slide 6: Our System
SRAM
GAME
FPGA SoC
Microblaze CPU
50MHz
Controller
Hardware
50MHz CLK
Graphic Output/
(Processor ?)
Sound ?

## Slide 7: Start with the controller
We are going to start with the controller
Create VHDL code to generate the signals and read the buttons press
Could be done by bit-banging on the CPU but we have the resources for all the timing to be done outside of the CPU
Later we will connect our hardware to the CPU

## Slide 8: Types of Controllers
Digital only
8 buttons
Digital used a Timer
Digital buttons
Analog direction
Digital buttons
Analog direction/buttons
Analog tilt direction

## Slide 9: NES Controller
NES Pin out
1
4
5
7
Ground - 1
Pulse (in) - 2
Latch (in) - 3
Data (out) - 4
Power - 7

## Slide 10: Interface
The latch tells the controller to capture the button state
The pulse moves each button through the data output
Latch is a 12us high signal
Pulse is 12us per cycle

## Slide 11: Xilinx Software
VHDL software is written in the ISE program
Start a new project and select the chip we are using
To connect the VHDL to pins we need to edit the UCF file

## Slide 12: VHDL Code
VHD File
entity top_level_test is
Port ( reset : in STD_LOGIC;
clk_50mhz : in STD_LOGIC;
buttonled : out STD_LOGIC_VECTOR (7 downto 0);
nes_latch : out STD_LOGIC;
nes_clk : out STD_LOGIC;
nes_data_in : in STD_LOGIC);
end top_level_test;

## Slide 13: Example
UCF File
NET "buttonled[0]" LOC = D4;
NET "buttonled[1]" LOC = C3;
NET "buttonled[2]" LOC = E6;
NET "buttonled[3]" LOC = D6;
NET "buttonled[4]" LOC = D13;
NET "buttonled[5]" LOC = A7;
NET "buttonled[6]" LOC = G9;
NET "buttonled[7]" LOC = A8;
NET "clk_50mhz" LOC = C9;
NET "nes_clk" LOC = N14;
NET "nes_data_in" LOC = E15;
NET "nes_latch" LOC = N15;
NET "reset" LOC = N17;