## Slide 1: Lab 2: Graphics Part 1

## Slide 2: Background on VGA
In the 1980s display standards started to be developed
CGA (Color Graphics Adapter) was created in 1981
  320x200 pixel mode
  640x200 pixel mode
  Each pixel is addressed able but only 4 colors available
  To have different sets of colors there were two palette modes (black, cyan, magenta, white) and (black, green, red, brown)

## Slide 3: CGA
Palette Mode 0
Palette Mode 1

## Slide 4: EGA
EGA (Enhanced Graphics Adapter) was created in 1984
Resolution increased to 640x350
Can display 16 colors
Still used a palette scheme. Could display 16 colors from a set of 64 total colors

## Slide 5: VGA
VGA (Video graphics Array) created in 1987
640x480
Each color is 6-bits giving a 262,144 color palette

## Slide 6: Compare color palette
6-bit RGB
EGA
Sega Master System
9-bit RGB
Sega Genesis

## Slide 7: Compare color
15-bit RGB
SNES
SVGA
Gameboy advance
18-bit RGB
VGA
Nintendo DS

## Slide 8: Color compare
24-bit RGB “True color”
SVGA
Nintendo 3DS

## Slide 9: NES Graphic
48 color palette
Resolution of 256x240 (only used 256x224)

## Slide 10: VGA
We are going to use the VGA standard for our SoC
Use the resolution of 640x480
Use same timing information
But use only 8 colors

## Slide 11: VGA

## Slide 12: VGA
We will have all the items done in pixel time
The pixel clock is the time to generate 1-pixel on the screen 25MHz
So for a horizontal row
Tdisp = time to display the row
640 pixel clocks
Tpw=pulse time
96 pixels
Tbp=back porch
48 pixels
Tfp=front porch
16 pixels
Ts = sync time
800 pixels

## Slide 13: VGA
A vertical refresh requires that all the rows are display
We can use the horizontal sync to count
Tdisp = time to display the screen
480 horizontal syncs
Tpw=pulse time
2 horiz syncs
Tbp=back porch
29 horiz syncs
Tfp=front porch
10 horiz syncs
Ts = sync time
521horiz syncs

## Slide 14: VGA UCF file

## Slide 15: Display File
You need to create a VHDL file that does all the timing to display the screen
This will be its own file do not mix it with the second part
It must output the x and y pixel coordinates, hsync, vsync, rgb

## Slide 16: VGA Test File
Using the display file you need to create a test file
Use the switches to determine a color to output

## Slide 17: Graphics in the video system
Screen resolution is 640x480
This gives us a total of 307,200
Each pixel will need 4-bits (R, G, B, transparent bit)
We add transparent bit because we will have a foreground and background
This will mean that we need to set aside video memory of 1,228,800 = 1.2Mbit [307,200bits for 320x240]
So to have a foreground and background we would need 2*1,228,800bits = 2,457,600bits
All the memory has to fit on our FPGA chip
The FPGA has 648Kbits of RAM

## Slide 18: Graphics on FPGA
We cannot store the complete video frame on our board
This is going to require that we rethink how to manage the graphics in our chips
We can reduce the resolution
To keep same screen ratio
  640x480
  320x240
  160x120

## Slide 19: Scaling
Monitor
640x480
FPGA memory
160x120
Upconvert on FPGA

## Slide 20: Up convert
Smaller screen resolution
Larger screen resolution
Each pixel is not a block of pixels

## Slide 21: Up convert
If we still use a lower screen resolution we still have a memory problem
It cost to much memory to store each pixel
We need a different way to store the screen to generate

## Slide 22: Sprites and Tiles
What we can do is on the graphic card store sprites
A sprite is a pre-created image we want to display
In memory we store the sprites
For animation we have multiple sprites.
Pacman open mouth
Pacman closed mouth

## Slide 23: Sprites and Tiles
This means we will need to place a limit on the number of sprites our game can support
We can always have the game software load in different sprites
Ex. We make pacman two players
Player one we can load in the sprite for pacman
Player two we con load in the sprite for ms. Pacman
We need a way to know where to place the sprites

## Slide 24: Sprites and Tiles
The screen is made up of a tile-map
The tile-map is a grid or 2D-array that tells which sprite to use

## Slide 25: Tile Map
=sprite 0
=sprite 1
=sprite 2
=sprite 3
The portion of
The tile map is
2 | 3 | 2
0 | 0 | 0
1 | 0 | 0

## Slide 26: Size of sprites and Tile-map
By using sprites and tile-map the memory requires are smaller
A tile map of 40x30 [screen resolution of 320x240]
  Requires 120 tiles
  Each tile requires n-bits where we have 2^n=sprites
  So say we have 32 sprites then we need 5-bits
  Size of memory 600 bits

## Slide 27: Sprites
Sprites will need to be a group of pixels
We will create sprites of 8x8
Size will be 64 pixels at 4-bits = 256bits
We have 32 sprites so 256*32 = 8,192bits
In total 600 bits for Tile-map + 8,192bits for sprites for a total of 8,792bits required ~8.8Kbits (to store each pixel need 307kbit so we reduce by 97%)
The FPGA has 648Kbits of RAM

## Slide 28: Sprite

## Slide 29: Lab
In this lab you will need to create two different screen resolutions with different grid sizes
This will be the start of your tile-map. Next lab we add the memory and sprites
320x240
  Create grid of 40x30
160x120
  Create grid of 20x15
Make each grid tile a different color

## Slide 30: Lab
You want each tile to have a way to index
Using the pixel_x and pixel_y you need to be able to index which tile in the tile-map
0 | 1 | 2 | 3
4 | 5 | 6 | 7
8 | 9 | 10 | 11
12 | 13 | 14 | 15

## Slide 31: To use memory
Architecture
  Constant cblue : std_logic_vector(2 downto 0) := “100”;
  Constant cgreen : std_logic_vector(2 downto 0) := “010”;
  Type tile_map is array(0 to 119) of std_logic_vector(2 downto 0);
  Signal grid_map : tile_map := (cblue, cred, cgreen, … );
  Signal mapindex : std_logic_vector(7 downto 0);
begin

## Slide 32
Mapindex <= ( place in here an express with type std_logic_vector);
Rgb <= grid_map(conv_integer(mapindex));
For conv_integer make sure you add
  use IEEE.NUMERIC_STD.ALL;
  use ieee.std_logic_arith.all;
  use ieee.std_logic_unsigned.all;